## Slide 1: Passive Solar Building Design Using Genetic Programming
M. Mahdi Oraei Gholami
Brock University
Dept. of Computer Science
500 Glenridge Ave.
St. Catharines, Ontario
L2S 3A1, Canada
mahdi.oraei@gmail.com
Brian J. Ross
Brock University
Dept. of Computer Science
500 Glenridge Ave.
St. Catharines, Ontario
L2S 3A1, Canada
bross@brocku.ca
GECCO 2014

## Slide 2: Introduction
Passive solar building design goals:
  Collect heat in winter
  Reject heat in summer
  No mechanical system
How to design a building?
  Computer aided design
  Interactive evolutionary systems
  Automated evolutionary systems

## Slide 3: Introduction
What affects a building design?
  Building location
  Local climate
  Materials
  Window and Shading: size and placement.
  Budget

## Slide 4: Objectives
Objectives
  Building designs having good solar performance
Performance may include...
  Cooling energy
  Heating energy
  Window heat gain
  …

## Slide 5: Approach
CFG-based system
  Modeling language.
  Building shape and size.
  Door and window.
  Materials.
Genetic programming
  Implements split grammar ideas and CFG expressions.
EnergyPlus
  Simulate and analyze all aspects of the building.

## Slide 6: Conflicting objectives
Heat Gain
  windows allow sunlight to heat interior in winter but results in air conditioning cost in summer
Heat Loss
  windows lose heat at night, which requires additional heating expense

## Slide 7: Single-objective evolution
Minimize Energy Usage
  small insulated shack with no windows and small door is very efficient to heat and cool.
Maximize solar heat gain
  Maximizes sun intake with its walls of windows on the east, south, and west sides.

## Slide 8: Background

## Slide 9: Evolutionary Design
Evolutionary design is the application of evolutionary computation in designing forms.
Architecture, art, engineering, etc.

## Slide 10: Design Language
Context free grammar design language.
Strongly typed GP.
Split grammar: simplified shape grammar
  Some aspects (roofs, windows,...) based on split grammar approach.

## Slide 11: Split Grammar
Rules:
Taken from [21]
Result:

## Slide 12: Energy Efficiency
Reducing the cost and the amount of energy, specially non-renewable energies, that is needed for providing services and products.
Practical result
  Saving energy
  Pollution is reduced.
  Reducing noise of mechanical devices.

## Slide 13: Energy Plus

## Slide 14: EnergyPlus
EnergyPlus is a free energy simulation, load calculation, building and energy performance, heat and mass balance application.
  http://apps1.eere.energy.gov/buildings/energyplus/

## Slide 15: EnergyPlus Input
1. Input data file (IDF)
  Materials, and Constructions
  Geometry: place and size of walls, roofs, floors, doors, windows, and overhang
  Lights & Electrical equipment
  Ideal Loads Air System
2. Weather file (EPW)
  Temperature
  Latitude, longitude
  wind, rain, snow
  ... and lots more!

## Slide 16: EnergyPlus Output
Annual Building Utility Performance
  Total energy
  Heating
  Cooling
Geometric characteristics:
  Building area
  Window area
  Wall area

## Slide 17: Literature Review

## Slide 18: Evolutionary Design and Energy Efficient Architecture
Malkawi et al. (2005) : Windows, supply airs ducts, and return air ducts placement.
Marin et al. (2008): Winter comfort.
Caldas (2008) : Sustainable energy-efficient buildings.
Turrin et al. (2010) : Large roofs structures.
Harrington (2012) : Summer and winter comfort.

## Slide 19: Methodology

## Slide 20: System Overview
ECJ : evolutionary system
GP: Strongly typed
CFG-guided design language with split grammar functions.
Energy Plus: simulation and analysis system.
Multi-objective technique: normalized rank-sum

## Slide 21: Multi-Objective Techniques Comparison
Fitness | Pareto Ranking | Ranks | NRS
(33,0,125,39) | 1* | (3,1,6,3) | 2.27
(30,24,38,18) | 1* | (2,3,3,2) | 1.4
(0,47,43,18) | 1* | (1,4,4,2) | 1.73
(78,62,2,0) | 1* | (6,6,1,1) | 1.37*
(43,19,20,79) | 1* | (4,2,2,4) | 1.47
(55,55,89,80) | 2 | (5,5,5,5) | 2.67

## Slide 22: GP Types and Functions
Type | Function
R | Add Root(S)
S | Add Cube(D,D,D,FF), Add Cube(D,D,D,F)
FF | First Floor(DG,G,G,G,R2,I)
F | Add Floor(G,G,G,G,R2,I)
DG | Add Door Grid(I,I,I,d,W,I)
G | Add Grid(I,I,W,I), Add Empty Grid(I)
DR | Add Door(D,D,I,I)
W | Add Window(D,D,I)
W | Add Window Overhang(D,D,D,D,D,I)

## Slide 23: GP Types and Functions ( cont.)
Type | Function
R2 | Add Simple Roof(I), Add Skylight(G)
R2 | Add Gabled Roof(I,G,G,D)
R2 | Add Gabled Roof2(I,G,G,D)
D (& I) | Avg(D,D),Max(D,D), Min(D,D), Mul(D,D), Div(D,D), IfElse(D,D,D,D), ERC
D | Half(D), halffwd(D)
I | Inc(I), dec(I)

## Slide 24: Roof, Overhangs, Skylights.
(a) Gabled roof 1.
(b) Gabled roof 2.
(c) Overhangs and skylights.
(d) Gabled & Skylight roof.

## Slide 25: Building Model and Its Grammar Tree.

## Slide 26: Constraints
Some of the constraints are as follows:
  Min/max size limits
  No interior design
  symmetric window placement per wall

## Slide 27: Experimental Setup

## Slide 28: GP Parameters
Parameter | Value
Number of Runs | 10
Generations | 100
Population Size | 300
Initialization Method | Half-and Half
Tournament Size | 3
Crossover Rate | 90%
Mutation Rate | 10%
Elitism | 2
Grow Tree Max Depth | 6
Grow Tree Min Depth | 2
Full Tree Max Depth | 12
Full Tree Min Depth | 5

## Slide 29: Design Parameters
Parameter | Value (m)
Max/Min Floor Length | 20/10
Max/Min Floor Width | 20/10
Max/Min Floor Height | 8/4
Maximum Number of Rows on a Façade | 2
Maximum Number of Columns on a Façade | 6
Max/Min Door Height | 8/2
Max/Min Door Width | 6/1
Max/Min Roof Height | 10/3

## Slide 30: Materials
Construction | Material | U-factor
Wall_1 | Wood, fiberglass quilt, and plaster | 0.516
Wall_2 | Wood, plywood, insulation, gypsum | 0.384
Wall_3 | Gypsum, air layer with 0.157 thermal resistance, gypsum | 1.978
Wall_4 | Gypsum, air layer with 0.153 thermal resistance, gypsum | 1.994
Wall_5 | Dense brick, insulation, concrete, gypsum plaster | 0.558
Roof_1 | No mass with thermal resistance 0.65 | 1.189
Roof_2 | Roof deck, fiberglass quilt, plaster | 0.314
Roof_3 | Roof gravel, built up roof, insulation, wood | 0.268
Floor_1 | Concrete, hardwood | 3.119
Floor_2 | Concrete, hardwood | 3.314

## Slide 31: Window and Door Materials
Construction | Material | U-factor | SHGC
Window_1 | 3 mm glass, 13 mm air, 3 mm glass | 2.720 | 0.764
Window_2 | 3 mm glass, 13 mm argon, 3 mm glass | 2.556 | 0.764
Window_3 | 6 mm glass, 6 mm air, 6 mm glass | 3.058 | 0.700
Window_4 | 6 mm low emissivity glass, 6 mm air, 6 mm low emissivity glass | 2.371 | 0.569
Window_5 | 3 mm glass | 5.894 | 0.898
Window_6 | 6 mm glass | 5.778 | 0.819
Door_1 | 4 mm wood | 2.875 | -
Door_2 | 3 mm wood, air, 3 mm wood | 4.995 | -
Door_3 | Single layer 3 mm glass | 5.894 | 0.716

## Slide 32: Different Geographical Locations Experiment

## Slide 33: Different Geographical Locations
Toronto, Canada
  (baseline) humid continental
Anchorage, Alaska
  northern subarctic.
Eldoret, Kenya
  equatorial, tropical.
Las Vegas, USA
  subtropical, hot desert.
Melbourne, Australia
  southern hemisphere, temperate.

## Slide 34: Objectives
1- Window heat gain in winter.
2- Annual cooling and heating energy consumption.
3- Window constraint: having at least 25% window area.

## Slide 35: Results

## Slide 36: Window Area Analysis
Location | South | West | North | East
Toronto | 94 | 27.5 | 24 | 35
Las Vegas | 87 | 28 | 25 | 28
Eldoret | 45 | 52.5 | 27.5 | 55
Anchorage | 89 | 26 | 22.5 | 28
Melbourne | 25 | 29 | 81.5 | 38
Window area percentage of top solutions.
Window Placement:
  North hemisphere: south.
  South hemisphere: north.
  Near equator: east and west.

## Slide 37: Performance Plots

## Slide 38: Scatter Plot

## Slide 39: Scatter Plot (cont.)
a- Worst model (Toronto)
b- Best model (Melbourne)

## Slide 40: Consistency: Toronto Models

## Slide 41: Best Models
Toronto
Anchorage
Las Vegas
Eldoret
Melbourne

## Slide 42: Best Models Analysis (cont.)
Neither skylights nor complex roofs are selected.
  Annual energy consumption increases in either cases.
  larger roofs = increased room volume
Size:
  Maximum length
  Maximum width.
  Height changes based on the location.
Materials:
  Walls: third lowest U-factor.
  Double pane windows with argon
    Second lowest in U-factor and the best in SHGC
  Floors and Roofs: biggest U-factor

## Slide 43: Multi-Floor Experiment

## Slide 44: Stylistic multi-floor buildings
Building name: Statoil Headquarters
Location: Fornebu, Norway.
Designed by: A-lab

## Slide 45: Multi-floor Experiment
Objectives:
  Window heat gain in winter
  Annual cooling and heating energy consumption.
  Exactly 35% window area.
  Each floor has to be 15% smaller than the floor underneath.
  Total volume has to be
Location: Toronto

## Slide 46: Multi-floor Experiment
Results:
  More energy consumption than when either window constraint or volume constraints are not considered.
  Less window heat gain than when window constraint is not considered.
  Without window constraint: volume constraints are met easier.
  Without volume constraints: window constraint is met easier.

## Slide 47: Multi-Floor Experiment
Materials:

## Slide 48: Performance Plots

## Slide 49: Performance Plots

## Slide 50: The Best Model

## Slide 51: The Best Model Heat Gain and Annual Energy

## Slide 52: Discussion
A comparison to Caldas (2008) work:
Similarities:
  Materials, roofs, doors, overhangs, and windows are considered in both.
  Multi-objective approach.
  Both have the problem of no window when only energy consumption is considered.
Differences:
  Illumination vs. window heat gain
  DOE2 vs. EnergyPlus
  GA vs. GP
  Two objectives vs. five objectives
  Pareto ranking vs. normalized rank sum

## Slide 53: Conclusion
Evolutionary design (GP)
  Highly performance building design
CFG based grammar guided system
  Walls, floors, roofs, windows, overhangs, materials
  Grammars were straightforward for our purpose
EnergyPlus
  Simulation and analysis system.
  Worked well, although it is not designed to be used in batch mode with 1000’s of simulations!

## Slide 54: Conclusion
  Multi-Objective
  Normalized rank sum worked well with even 5 objectives.
  Trade-off of objectives: Energy objectives treated “equally”, with no preferred biases.
Consistent solutions with respect to size, geometry, materials, and design elements are achieved in all experiments.

## Slide 55
Thank you